## Slide 1: UART
Universal Asynchronous Receiver/Transmitter
Michael Mollica

## Slide 2: History Of UART
Gordon Bell – Digital Equipment Corporation (1960’s)
Idea was to create a “Universal” communication protocol
  Data Format
  Transmission Speed
Less common in modern electronics due to USB and Ethernet protocols

## Slide 3: BACKGROUND

## Slide 4: Asynchronous vs. Synchronous
NO CLOCK
Combinational Logic
Push Buttons
Switches
CLOCK
Flip-Flops
State Machines
Processors
*Note: UART still requires speed to be configured even though it does not operate with a clock.

## Slide 5: Serial Communication
Simplex / Half Duplex / Full Duplex
Receiver & Transmitter
Bits are sent/received one at a time
Much more widely used compared to Parallel Communication
  Trouble in High Frequency Systems

## Slide 6: UART Connectivity
Two lines for serial data (Rx, Tx)
One line for common ground
Device 1 Rx connects to Device 2 Tx (and vice versa)
1 Master and 1 Slave
Both devices must have the same Baud Rate

## Slide 7: Baud Rate
Baud Rate != Bit Rate
Bit Rate = # of Bits / Time
  Alternatively, Bit Rate = Baud Rate x Bits per symbol
Baud Rate = # of symbols / Time
9600, 57600, 115200, etc.

## Slide 8: UART Packet
Data is sent in packets
Packets contain: Start bit, Stop bit, Parity bits, and Data bits
Start bit denotes the beginning of a data frame and begins the process of reading in the UART (Usually LOW)
Parity bits are used for error checking (Even, Odd)
Stop bit(s) denotes the end of a data frame (Usually HIGH)

## Slide 9: HARDWARE

## Slide 10
ATMega8U2 USART Block Diagram (Chip on Arduino UNO) [3]

## Slide 11: Key Hardware Components
Parity Generator
  Even Parity = Dn-1 xor … xor D1 xor D0 xor 0
  Odd Parity = Dn-1 xor … xor D1 xor D0 xor 1
Clock Recovery
  Synchronizes the receiver input with the system clock
Data Recovery
  Samples each received bit three times and outputs the majority value
Parity Checker
  Compares receiver parity bit with calculated parity
UDR (Transmit & Receive)
  Buffer used to store transmitted and received data (FIFO)

## Slide 12: SOFTWARE
*Particularly for Arduino

## Slide 13: UART Configuration
Software must initialize the following:
Baud Rate
Parity
Data Bits
Arduino Serial Functions:
Serial.begin(BR)  void
Serial.available()  bool
Serial.read()  byte
Serial.write(val)  void

## Slide 14: Why Choose UART?
Advantages
No Clock required
Two wires needed
Error checking
Modifiable data packet
Long distance (Up to 1000 meters)
No addressing needed
Disadvantages
One-to-One communication
Must configure Baud Rate
9-bit maximum data packet

## Slide 15: Application in Capstone
Send shifter data captured on Arduino UNO to Arduino Mega Master MCU
UART sends shifter position at 115200 Baud Rate
Master MCU connection
Shifter MCU connectivity

## Slide 16: Sources
[1] UART: A Hardware Communication Protocol Understanding Universal Asynchronous Receiver/Transmitter | Analog Devices
[2] Baud Rate and its importance – GeeksforGeeks
[3] ATmega8U2 | Microchip Technology
[4] What is UART? Basics of UART | Instrumentation and Control Engineering (automationforum.co)
[5] UARTs Provide Reliable Serial Communication | DigiKey